## Slide 1: Water
Dr. Bharati Choudhari
Asst. Professor- S&H
KJSCE, SVU,
Vidyavihar.

## Slide 2
Introduction
1). Like air, water is one of the few basic materials which is of prime importance for the preservation of life on this earth.
2). All are aware of the uses of water for drinking, cooking, cooking, bathing & for farming etc.
3). But few know the importance of water as an engineering material.
4). As an engineering material water is used for producing steam, in boilers to generate hydro-electric power, furnishing steam for engines, for construction of concrete structures for manufacturing purposes & as a solvent in chemical process.

## Slide 3
Sources of Water:
The Main Sources Of Water Are:
1). Rain water
2). River water
3). Spring or well water
4). Sea water

## Slide 4
Types of impurities in water:
The impurities present in water are classified as:
1). Dissolved impurities: dissolved impurities may organic or inorganic.
Inorganic impurities: the carbonates, bicarbonates, sulphates, chlorides of calcium, magnesium, iron potassium and aluminium.
Organic impurities: Organic water products, amino acids, proteins, etc. Gases: O2, CO2, Oxides of nitrogen and sulphur, H2S etc.

## Slide 5
2). Suspended impurities: It is of two types:
Inorganic- sand & clay;
Organic- vegetable and animal matter.
3) Biological Impurities: Micro-organisms like pathogenic bacteria, fungi, algae, etc.

## Slide 6
DISADVANTAGES OF HARDWATER/ CAUSES OF HARDNESS:
The following are the disadvantages when hard water is used for various purpose:
DOMESTIC USE:
Washing and Bathing: Hard water does not form lather easily with soap, so soap is wasted
(b) Drinking: Hard water causes bad effects on our digestive system. Sometimes, stone formation takes place in kidneys

## Slide 7
(c) Cooking: The boiling point of water is increased due to the presence of salts. Hence, more fuel and time are required for cooking.
(ii) INDUSTRIAL USE:
Textile Industry: Hard water causes wastage of soap. Precipitates of calcium and magnesium soap adhere to the fabrics and cause problem such difference in color shades, dull shades, patches, etc.
Paper Industry: Calcium and Magnesium salts in water may affect the quality of paper.

## Slide 8
(c) Sugar Industry: Water containing sulphates, carbonates, nitrates affects the crystallisation of sugar.
(d) Pharmaceutical Industry: Hard water may form some undesirable products while preparation of pharmaceutical products.

## Slide 9
(iii) STEAM GENERATION IN BOILERS: For steam generation, boilers are employed. If hard water is used in boilers, It may lead to the following troubles-
Boiler Corrosion
Scale and Sludge formation.
Priming and Foaming
Caustic embrittlement Pharmaceutical industry

## Slide 10
HARDNESS OF WATER (OR) HARDWATER AND SOFT WATER:
Hard Water: The water which does not produce lather (or) very little lather with soap is called Hard Water.
Soft Water: Soft water readily produces a lot of lather when mixed with little soap.
The Hardness of water is caused by the presence of dissolved salts such as Bicarbonates, Sulphates, Chlorides and Nitrates of bivalent metal ions like Ca+2 & Mg+2.

## Slide 11
Soap is sodium/ potassium salt of higher fatty acids like stearic, oleic and palmetic acids. When soap is mixed with soft water lather is produced due to stearic acid and sodium stearate.
Na – Stearate + H2O  NaOH + Stearic Acid
[C17H35COOH]
Stearic Acid + Na-Stearate  Formation of lather.

## Slide 12
When soap comes in contact with HARD WATER, Sodium stearate will react with dissolved calcium and magnesium salts and produce calcium stearate or magnesium stearate which is white precipitate.
2Na– Stearate + Ca+2  Ca– Stearate↓ + 2Na+
[2C17H35COONa] + Ca+2  [(C17H35COO)2Ca]↓ + 2Na+ (Soap) (Soluble) (Insoluble) (Soluble)
[2C17H35COONa] + Mg+2  [(C17H35COO)2Mg]↓ + 2Na+ (Soluble) (Soluble) (Insoluble) (Soluble)

## Slide 13
TYPES OF HARDNESS
The hardness of water is of two types-
Temporary hardness (or) Carbonate hardness
Permanent hardness (or) Non-Carbonate hardness
(1) Temporary Hardness: Temporary hardness is caused by two dissolved bicarbonate salts Ca(HCO3)2 and Mg(HCO3)2. The hardness is called “Temporary Hardness” because it can be removed easily by means of boiling.
Ca(HCO3)2 + Heating  CaCO3↓ + H2O + CO2↑ Mg(HCO3)2 + Heating  Mg(OH)2↓ + 2CO2↑

## Slide 14
(2) Permanent Hardness: Permanent hardness of water is due to the dissolved chlorides, sulphates and nitrates of calcium and magnesium. These salts are CaCl2, CaSO4, Ca(NO3)2, MgCl2, MgSO4, Mg(NO3)2. These hardness cannot be removed easily by boiling. Hence it is called “Permanent Hardness”. Only chemical treatment can remove this hardness.
Total Hardness Of Water = Temporary Hardness + Permanent Hardness

## Slide 15
DEGREE OF HARDNESS:
• The Concentration of hardness as well as non-hardness constituting ions are, usually expressed in the term of “Equivalent amount of CaCO3”
• Since this mode permits the multiplication and division concentration, when required.
• The choice of CaCO3 in particular is due to its molecular weight (m.wt.) is “100” (Equivalent wt. = 50), and
• Moreover, it is insoluble salt that can be precipitated in water treatment.

## Slide 16
Therefore, 100 parts by weight of CaCO3 hardness must be equivalent to-
162 parts by weight of Ca(HCO3)2 hardness
146 parts by weight of Mg(HCO3)2 hardness
136 parts by weight of CaSO4 hardness
111 parts by weight of CaCl2 hardness
164 parts by weight of Ca(NO3)2 hardness
120 parts by weight of MgSO4 hardness
146 parts by weight of MgCl2 hardness
148 parts by weight of Mg(NO3)2 hardness

## Slide 17
Salt | Molar Mass | Chemical Equivalent | Multiplication Factor
Ca(HCO3)2 | 162 | 81 | 100/ 162
Mg(HCO3)2 | 142 | 73 | 100/ 142
CaSO4 | 136 | 68 | 100/ 136
FeCl2 | 127 | 63.5 | 100/ 127
CaCl2 | 111 | 55.5 | 100/ 111
MgSO4 | 120 | 60 | 100/ 120
MgCl2 | 95 | 47.5 | 100/ 95
CaCO3 | 100 | 50 | 100/ 100
MgCO3 | 84 | 42 | 100/ 84
CO2 | 44 | 22 | 100/ 44
Ca(NO3)2 | 164 | 82 | 100/164
Mg(NO3)2 | 148 | 74 | 100/ 148
HCO3- | 61 | 61 | 100/ 122
OH- | 17 | 17 | 100/ 34
CO32- | 60 | 30 | 100/ 60

## Slide 18
Salt | Molar Mass | Chemical Equivalent | Multiplication Factor
NaAlO2 | 82 | 82 | 100/ 164
Al2(SO4)3 | 342 | 57 | 100/ 114
FeSO4.7H2O | 278 | 139 | 100/ 278
H+ | 1 | 1 | 100/ 2
HCl | 36.5 | 36.5 | 100/ 73
The method of calculating degree of hardness is given by the following formula
•Hardness causing salt in terms of equivalent of CaCO3= (Amount (Mass) of the hardness causing salt x 100)/ Molecular weight of hardness causing salt

## Slide 19
UNITS OF HARDNESS:
The 5 different units in which the hardness of water is expressed as given below-
(1) Parts per million (PPM): PPM is the number of parts of CaCO3 equivalent hardness per 106 parts of water.
i.e., 1 PPM = 1 part of CaCO3 equivalent hardness in 106 parts of water.

## Slide 20
(2) Milli grams Per Litre (mg/litre): mg/L is the number of milligrams of CaCO3 equivalent hardness present per litre of water.
i.e., 1 mg/L = 1 mg of CaCO3 equivalent hardness in 1L of water.
But 1 L water weighs = 1 kg of water
1 kg = 1000 gms = 1000 x 1000 mg = 106 mg
∴ 1 mg/L = 1mg of CaCO3 equivalent per 106 mg of water
= 1 part of CaCO3 equivalent per 106 parts of water
∴ 1 mg/L = 1 ppm

## Slide 21
(3) Degree Of Clarke (oCl): It is number of grains (1/7000 lb) of CaCO3 equivalent hardness per gallon (10 lb) of water.
(or) It is defined as the number of parts of CaCO3 equivalent hardness per 70,000 parts of water.
∴ 1 oCl = 1 grain of CaCO3 eq. hardness per gallon of water.
(or) 1 oCl = 1 part of CaCO3 eq. hardness per 70,000 parts of water
∴ 1 ppm = 0.07 oCl

## Slide 22
(4) Degree Of French (oFr): It is the number of parts of CaCO3 equivalent hardness per 105 parts of water.
1 oFr = 1 part of CaCO3 equivalent hardness per 105 parts of water
∴ 0.1 oFr = 1 ppm
Note: The hardness of water can be converted into all the four units by making use of the following interconversion formula-
1 ppm = 1mg/L = 0.07oCl = 0.1oFr
1 oCl = 1.43oFr = 14.3 ppm = 14.3 mg/L

## Slide 23
(5) Milliequivalent per Litre (meq/L): It is the number of milliequivalent of hardness present per litre of water.
1 meq/L= 1 meq of CaCO3 per litre of water
= 10-3 x 50 g of CaCO3 eq. of hardness per litre of water
= 50 mg of CaCO3 eq. of hardness per litre of water
= 50 mg/L of CaCO3 eq.
= 50 ppm
1 meq/L= 50 ppm

## Slide 24
PROBLEM:
A sample of water gives an analysis 13.6 mg/L of CaSO4 , 7.3 mg/L of Mg(HCO3)2 . Calculate the total hardness and permanent hardness.
Sol:
Total hardness= Temporary hardness + Permanent Hardness = 5 + 10 = 15 mg/L = 15 ppm
Permanent hardness = 10 ppm
Temporary hardness= 5 ppm
Salt | Quantity (mg/L) | M. Wt. | Multiplication Factor | Eq. of CaCO3 | Hardness
CaSO4 | 13.6 | 136 | 100/ 136 | 13.6 x (100/ 136)= 10 | P
Mg(HCO3)2 | 7.3 | 146 | 100/ 146 | 7.3 x (100/ 146)= 5 | T

## Slide 25
DETERMINATION OF HARDNESS OF WATER BY EDTA METHOD:-
This is a Complexometric titration method where Ethylenediamine tetraacetic acid (EDTA) is used.
EDTA forms complexes with different metal ions at different pH.
Calcium & Magnesium ions form complexes with EDTA at pH 9- 10.
To maintain the pH 9- 10 NH4Cl, NH4OH buffer solution is used.

## Slide 26
4. The disodium salt of EDTA is used for complexation.
5. An alcoholic solution of Eriochrome Black-T (EBT) is used as an indicator.
EDTA
EDTA disodium salt
Metal-EDTA complex

## Slide 27
BASIC PRINCIPLE:
When hard water comes in contact with EDTA, at pH 9- 10, the Ca+2 & Mg+2 forms stable, colourless complex with EDTA.
Ca+2 + EDTA + pH 9-10  Ca-EDTA
Mg+2 + EDTA + pH 9-10  Mg-EDTA

## Slide 28
Working:-
To the hard water sample, the alcoholic blue coloured EBT indicator is added along with the NH4Cl + NH4OH buffer (pH 9- 10) solution.
EBT forms an unstable wine-red complex with Ca+2 & Mg+2.
(Ca+2 + Mg+2) + EBT + Buffer (pH 9-10)  (Ca-EBT + Mg-EBT) complex
(Hard water) (Indicator) (Unstable wine-red complex)
This wine-red coloured [Ca-EBT & Mg-EBT] complex is then titrated against EDTA; when EDTA replaces EBT from Ca-EBT & Mg-EBT complex and forms stable colourless [Ca-EDTA] & [Mg-EDTA] complex releasing the blue coloured indicator EBT into H2O.
[Ca-EBT + Mg-EBT] complex + EDTA  EBT + [Ca-EDTA + Mg-EDTA] complex
(Unstable wine-red complex) (Blue) (Stable colourless complex)
Hence the colour change at the end point is wine-red to blue colour.

## Slide 29
The titration is carried out in the following steps 1. PREPARATION OF STANDARD HARD WATER: Dissolve 1gm of pure, dry CaCO3 in minimum quantity of dilute HCl and evaporate the solution to dryness on a water-bath. Dissolve the residue in distilled water to make 1 litre in a standard flask and shake well.
Molarity of standard hard water solution =
wt. of CaCO3 = 1 = 0.01M
M.wt. of CaCO3 100

## Slide 30
(2) PREPARATION OF EDTA SOLUTION:
Dissolve 4 gms of pure EDTA-disodium salt crystals along with 0.1 gm of MgCl2 in one litre of distilled water.
(3) PREPARATION OF INDICATOR (EBT):
Dissolve 0.5 gms of Erichrome Black-T in 100 ml of alcohol.
(4) PREPARATION OF BUFFER SOLUTION: Add 67.5 gm of NH4Cl to 570 ml of concentrated ammonia solution and dilute with distilled water to one litre

## Slide 31
(5) STANDARDISATION OF EDTA SOLUTION: Pipette out 20 ml of standard hard water solution into a conical flask. Add 2- 3 ml of buffer (pH 9- 10) solution and 2- 3 drops of EBT indicator. Titrate the wine-red coloured complex with EDTA taken in a burette after rinsing it with EDTA solution till the wine red colour changes to clear blue.
Note the burette reading and let the volume be “x”ml. Repeat the titration to get concurrent values.

## Slide 32
(6) TITRATION OF SAMPLE HARD WATER (Total) :
Pipette out 20 ml of the water sample into a 250ml conical flask, add 2- 3 ml of buffer (pH 9- 10) solution and 2- 3 drops of EBT indicator. Titrate the wine-red coloured solution with EDTA taken in the burette till a clear blue coloured end point is obtained.
Let the volume of EDTA be “y” ml. Repeat the titration to get concurrent values

## Slide 33
(7) TITRATION FOR PERMANENT HARDNESS:
Pipette out 100 ml of hard water sample in a beaker and boil till the volume reduces to 20 ml. All the bicarbonates of Ca++ and Mg++ decomposes to CaCO3 and Mg(OH)2. Cool the solution and filter the water into a flask, wash the beaker and precipitate with distilled water and add the washing to conical flask. Add 2- 3 ml of buffer (pH 9- 10) solution and 2- 3 drops of EBT indicator and titrate with EDTA solution taken in the burette till a clear blue colour end point is obtained.
Note the burette reading. Let the volume be “z” ml.

## Slide 34
CALCULATIONS:
Molarity of standard hard water solution = 0.01 M.
(Calculated in the preparation of standard hard water)
Molarity of EDTA solution (M2 ): V1M1 = V2M2
n1 n2
n1 & n2 are no. of moles of Ca+2 and EDTA = 1 each
i.e., n1=1, n2=1
V1 = volume of standard hard water
M1= Molarity of standard hard water
V2= volume of EDTA
M2= molarity of EDTA
M2 = V1M1 = 20 X 0.01
V2 x (titre value)

## Slide 35
Molarity of sample hard water (M3 ):
V2M2 = V3M3
n2 n3
V2= volume of EDTA
M2= molarity of EDTA
V3= volume of sample hard water
M3= Molarity of sample hard water
M3 = V2M2 = M2 x y (titre value)= y x 0.01
V3 20 x
Total Hardness Of Water
= M3 x 100 gms/1 litre
=M3 X 100 X 1000mg/L or ppm= (y/ x) X 1000ppm

## Slide 36
Permanent Hardness Of Water:
V2M2 = V4M4 M4= V2M2 = zM2 = z X 0.01
n2 n4 V4 20 x
V2= volume of EDTA
M2= molarity of EDTA
V4 = volume of water sample containing permanent hardness (100 ml)
M4= Molarity of water sample containing permanent hardness
Permanent Hardness Of The Water Sample
= M4 x 100 x 1000 ppm
= z/ x X 1000ppm

## Slide 37
Temporary Hardness Of The Water Sample
= (Total Hardness – Permanent Hardness)
= (M3 x 100 x1000 – M4 x 100 x1000) ppm
= (M3 – M4) x 100 x1000 ppm
= (y-z) X 1000 ppm
x

## Slide 38
Problem:
1 gm of CaCO3 was dissolved in HCl and the solution was made upto 1 Lit with distilled water. 50 ml of the above solution required 30 ml of EDTA solution for titration. 50 ml of hard water sample required 40 ml of the same solution of EDTA for titration. 50 ml of the hard water after boiling, filtering, etc. required 30 ml of the same EDTA solution for titration. Calculate the temporary hardness of the water.

## Slide 39
Soln:
Molarity of CaCO3 (SHW) solution (M1)= 1/100= 0.01 M Molarity of EDTA solution (M2 ) = V1 M1/ V2
V1= volume of CaCO3 solution = 50 ml
M1= Molarity of CaCO3 solution = 0.01 M
V2= volume of EDTA = 30 ml
M2= 50 x 0.01/ 30 = 0.016 M
Molarity of Hard Water Sample Sol.(M3 )= V2M2/ V3
V2= volume of EDTA = 40 ml
M2= Molarity of EDTA = 0.016 M
V3= volume of hard water sample= 50 ml
M3= 40 x 0.016/ 50 = 0.0128 M

## Slide 40
Total Hardness of water
= 0.0128 x 100 x 1000
= 1280 ppm
Permanent hardness of water: = V4 M4 = V2 M2
n4 n2
M4 = V2M2/ V4
n4=1; V2= volume of EDTA = 30 ml
n2=1; M2= molarity of EDTA = 0.016
V4= volume of permanent hardness containing water = 50
M4 = 30 x 0.016/ 50= 0.0096 M

## Slide 41
Permanent hardness of water
= 0.0096 x 100 x 1000 = 960 ppm
Temporary hardness
= Total hardness – Permanent hardness
= 1280 – 960 = 320 ppm